Listed below is the information retrievable from the various connections.

- A1 Transmission

- B1 Climate Control

- A2 Fuel System

- B2 Cruise Control

- A3 ABS

- B5 SRS

- A5 TCU (Transmission Control)

- B6 Power Seat

- A6 Ignition System

- A7 Combined Instrument

### How to Use the Jumpers

Normally “Check Engine Light” information will be found in A2. Put the jumper into A2 and push the black button for one second. Count the red LED light as it blinks back information, blink, blink, pause, blink, blink, blink, pause, blink, blink, is an example of the response you would receive. 2-3-2 would be the code retrieved, now push the button again for one second, again count the blinks, keep checking for codes until one of them repeats, this means you have read all the codes.

### Clearing Codes on your 850

Now to clear the codes, push and hold the button for 6-7 seconds, release and as soon as the LED comes on push and hold the button for another 6-7 seconds. Now push the button for one second and read the codes again, you should get 1-1-1 (no faults).

### You Must Read All Codes before Clearing

Turn the ignition off and then start the car, the check engine light should be out. It is always a good idea to check for codes, clear them and then drive the vehicle to see if they return before replacing parts. The transmission can ask the check engine light to be turned on, so if you try clearing A2 codes and they wont go away try reading the transmission (A1), clear them , and then go back to A2.

| On Board DTC Code | Generic OBD Code Meaning |
| --- | --- |
| A1 — Transmission |  |
| 111 | No faults found |
| 112 | Solenoid S1 short circuit to battery voltage |
| 113 | Transmission control module (TCM) fault |
| 114 | Program selector open circuit or short circuit to supply |
| 121 | Solenoid S1 short circuit to ground or control module fault |
| 122 | Solenoid S1 open circuit |
| 123 | Solenoid STH short circuit to battery voltage |
| 124 | Mode selector faulty or short circuit to ground |
| 131 | Solenoid STH open/short circuit or control module fault |
| 132 | Transmission control module(TCM) fault |
| 134 | Faulty load signal from ignition control module |
| 141 | Oil temperature sensor short circuit to ground |
| 142 | Oil temperature sensor open circuit |
| 143 | Kickdown switch faulty or short to ground |
| 211 | Transmission control module (TCM) fault |
| 212 | S2 solenoid short circuit to battery |
| 213 | Throttle position (TPS) signal too high |
| 221 | S2 solenoid short circuit to ground or control module fault |
| 222 | S2 solenoid open circuit |
| 223 | Throttle position (TPS) sensor signal too low |
| 231 | Throttle position (TPS) sensor sporadic |
| 232 | Speedometer signal missing |
| 233 | Incorrect speedometer signal |
| 235 | High Oil temperature |
| 245 | Open or short in Torque limiting circuit |
| 311 | RPM signal from transmission missing |
| 312 | RPM signal from transmission faulty |
| 313 | Faulty signal from gear position sensor (PNP) |
| 321 | Shift time too long |
| 322 | Incorrect gear ratio |
| 323 | Lock up slips or is not engaged |
| 331 | Short circuit to battery in SL circuit |
| 332 | SL solenoid open or control module fault |
| 333 | SL solenoid short or control module fault |
| A2 — Fuel System |  |
| 111 | No faults detected |
| 112 | Fault in ECM |
| 115 | Injector 1 |
| 121 | MAF sensor signal |
| 123 | ECT signal |
| 125 | Injector 2 |
| 131 | RPM sensor signal missing |
| 132 | Battery voltage |
| 135 | Injector 3 |
| 143 | Front knock sensor signal |
| 145 | Injector 4 |
| 153 | Rear HO2S signal |
| 154 | EGR system leakage |
| 155 | Injector 5 |
| 212 | Front HO2S signal |
| 214 | RPM sensor signal sporadic |
| 223 | IAC valve opening signal |
| 225 | A/C pressure sensor signal |
| 231 | Long term fuel trim, part load |
| 232 | Long term fuel trim, idling |
| 233 | Long term idle air trim |
| 241 | EGR system flow malfunction |
| 245 | IAC valve closing signal |
| 311 | VSS signal |
| 314 | CMP sensor signal |
| 315 | EVAP system |
| 325 | Memory failure |
| 335 | Request for MIL lighting from TCM |
| 411 | TP sensor signal |
| 413 | EGR temp sensor signal |
| 414 | Boost pressure regulation |
| 416 | Boost pressure reduction from TCM |
| 432 | Temperature warning level 1 |
| 433 | Rear knock sensor signal |
| 435 | Front HO2S slow response |
| 436 | Rear HO2S compensation |
| 443 | Three way cat. Efficiency |
| 444 | Acceleration signal |
| 451 | Misfire cylinder 1 |
| 452 | Misfire cylinder 2 |
| 453 | Misfire cylinder 3 |
| 454 | Misfire cylinder 4 |
| 455 | Misfire cylinder 5 |
| 513 | Temperature warning level 2 |
| 514 | Engine cooling fan low speed signal |
| 521 | Front HO2S Preheating |
| 522 | Rear HO2S Preheating |
| 531 | Power stage group A |
| 532 | Power stage group B |
| 533 | Power stage group C |
| 534 | Power stage group D |
| 535 | TC control valve signal |
| 541 | EVAP valve signal |
| 542 | Misfire more than one cylinder |
| 543 | Misfire at least one cylinder |
| 544 | Misfire more than one cylinder, three way cat damage |
| 545 | Misfire at least one cylinder, three way cat damage |
| 551 | Misfire cylinder 1, three way cat damage |
| 552 | Misfire cylinder 2, three way cat damage |
| 553 | Misfire cylinder 3, three way cat damage |
| 554 | Misfire cylinder 4, three way cat damage |
| 555 | Misfire cylinder 5, three way cat damage |
| A3 — ABS |  |
| 111 | No DTC set |
| 121 | Left front wheel sensor, faulty signal 122 Right front wheel sensor, faulty signal 123 Left rear wheel sensor, faulty signal 124 Right rear wheel sensor, faulty signal 40 km/h |
| 322 | Right front wheel sensor, irregular >40 km/h |
| 323 | Left rear wheel sensor, irregular >40 km/h |
| 324 | Right rear wheel sensor, irregular >40 km/h |
| 411 | Left front wheel inlet valve, open/short |
| 412 | Left front wheel return valve, open/short |
| 413 | Right front wheel inlet valve, open/short |
| 414 | Right front wheel return valve, open/short |
| 415 | Rear valve open/short |
| 421 | Rear wheel inlet valve circuit, open/short |
| 422 | Rear wheel return valve circuit, open/short |
| 423 | Traction control system valve, open/short |
| 424 | Pressure switch for TRACS, faulty or short circuit |
| 441 | Control module faulty |
| 442 | Pump pressure low |
| 443 | Pump motor, electrical or mechanical fault |
| 444 | No power supply to valves in hydraulic unit |
| A6 — Ignition |  |
| 111 | No DTC set |
| 112 | Control Module fault |
| 123 | Engine Coolant Temperature Sensor (ECT) from Control module missing or faulty |
| 131 | Engine speed (RPM) sensor signal missing |
| 142 | Control Module Fault |
| 143 | Knock sensor (KS) missing or faulty |
| 144 | Ignition control module load signal missing |
| 154 | EGR system flow too high in system |
| 214 | Engine speed (RPM) sensor signal missing sporadically |
| 224 | Engine Coolant Temperature sensor (ECT) signal missing or faulty |
| 234 | Throttle Position (TPS) signal missing at idle |
| 241 | EGR system flow too low in system |
| 243 | Throttle Position sensor (TPS) signal missing at idle |
| 311 | Vehicle speed signal missing or faulty |
| 314 | Camshaft Position sensor (CMP) signal missing or faulty |
| 324 | Camshaft Position sensor (CMP) signal missing sporadically |
| 411 | Throttle position sensor (TPS) signal from fuel injection system missing or faulty |
| 413 | EGR temperature sensor signal faulty |
| 432 | Control module box temperature too high level 1 |
| 433 | Knock sensor (KS) signal missing or faulty |
| 513 | Control module box temperature too high, level 2 |
| A7 — Combined Instrument (Trip Computer) |  |
| 112 | Fuel gauge short circuit |
| 113 | Fuel gauge open circuit |
| 121 | Temp. sensor interval too short |
| 122 | Temp. sensor interval too long |
| 123 | Digital output 48 pulse short circuit to supply |
| 131 | Digital output 12 pulse short circuit to supply |
| 132 | No RPM sensor signal |
| 133 | Tank signal to trip computer short to supply |
| B1 — Electronic climate control |  |
| 111 | No fault |
| 121 | Outside temperature sensor shorted to ground |
| 122 | Outside temperature sensor open circuit or shorted to 12 volts |
| 123 | Driver’s side interior temperature sensor shorted to ground |
| 124 | Driver’s side interior temperature sensor open circuit or shorted to 12 volts |
| 125 | Passenger’s side interior temperature sensor shorted to ground(earth) |
| 126 | Passenger’s side interior temperature sensor open circuit or shorted to 12 volts |
| 131 | Driver’s side air duct temperature sensor shorted to ground(earth) |
| 132 | Driver’s side air duct temperature sensor open circuit or shorted to 12 volts |
| 133 | Passenger’s side air duct temperature sensor shorted to ground(earth) |
| 134 | Passenger’s side air duct temperature sensor open circuit or shorted to 12 volts |
| 135 | No signal from engine coolant temperature sensor |
| 141 | Faulty signal from driver’s side temperature selector switch |
| 143 | Faulty signal from passenger’s side temperature selector switch |
| 145 | Faulty signal from function selector switch |
| 151 | Signal from fan speed sensor missing or too high |
| 152 | Signal from fan speed sensor shorted to earth |
| 211 | Driver’s side damper motor position sensor open circuit or shorted to 12 volts |
| 212 | Driver’s side damper motor position sensor shorted to earth |
| 221 | Passenger’s side damper motor position sensor open circuit or shorted to 12 volts |
| 222 | Passenger’s side damper motor position sensor shorted to earth |
| 231 | Ventilation damper motor position sensor open circuit or shorted to 12 volts |
| 232 | Ventilation damper motor position sensor shorted to earth |
| 233 | Floor/defrost damper motor position sensor open circuit or shorted to 12 volts |
| 234 | Floor/defrost damper motor position sensor shorted to earth |
| 235 | Recirculation damper motor position sensor open circuit or shorted to 12 volts |
| 236 | Recirculation damper motor position sensor shorted to earth |
| 311 | Driver’s side damper motor shorted to earth or shorted to 12 volts |
| 312 | Passenger’s side damper motor shorted to earth or shorted to 12 volts |
| 313 | Ventilation damper motor shorted to earth or shorted to 12 volts |
| 314 | Floor/defrost damper motor shorted to earth or shorted to 12 volts |
| 315 | Recirculation damper motor shorted to earth or shorted to 12 volts |
| 321 | Driver’s side damper motor active too long |
| 322 | Passenger’s side damper motor active too long |
| 323 | Ventilation damper motor active too long |
| 324 | Floor/defrost damper motor active too long |
| 325 | Recirculation damper motor active too long |
| 411 | Blower fan seized or drawing excessive current |
| 412 | Driver’s side interior temperature sensor inlet fan shorted to earth |
| 413 | No control voltage at driver’s side interior temperature sensor inlet fan |
| 414 | Driver’s side interior temperature sensor inlet fan seized |
| 415 | Passenger’s side interior temperature sensor inlet fan shorted to earth |
| 416 | No control voltage at passenger’s side interior temperature sensor inlet fan |
| 417 | Passenger’s side interior temperature inlet fan seized |
| 418 | No control signal to blower fan power stage |
| 419 | Faulty diagnostic signal from blower fan power stage |
| 420 | ECU fault in program memory |
| 511 | Damper motor limit position self-adjustment not carried out |
| B2 — Cruise Control |  |
| 111 | No faults detected |
| 112 | Abnormal speed signal |
| 122 | Speed has not exceeded 22mph or no speed signal |
| 211 | Control module malfunction |
| 212 | Malfunction in the circuit to the vacuum pump or regulator |
| B5 — SRS |  |
| 111 | No fault detected |
| 112 | Sensor module fault |
| 127 | SRS lamp open/short circuit |
| 211 | Drivers airbag short circuit |
| 212 | Drivers airbag open circuit |
| 213 | Drivers airbag short circuit to ground |
| 214 | Drivers airbag short circuit to supply |
| 221 | Passenger airbag short circuit |
| 222 | Passenger airbag open circuit |
| 223 | Passenger airbag short circuit to ground |
| 224 | Passenger airbag short circuit to supply |
| 231 | Left belt tensioner short circuit |
| 232 | Left belt tensioner open circuit |
| 233 | Left belt tensioner short circuit to ground |
| 234 | Left belt tensioner short circuit to supply |
| 241 | Right belt tensioner short circuit |
| 242 | Right belt tensioner open circuit |
| 243 | Right belt tensioner short circuit to ground |
| 244 | Right belt tensioner short circuit to supply |